## Slide 1: Python Workshop - Raspberry Pi -
2017년 8월
서강대학교

## Slide 2: 보조 도구들
Online White Board
  http://bit.ly/2017sopython1
Shared List
  http://bit.ly/2017sopython2
온라인 자료
  https://www.python.org/
  http://byteofpython-korean.sourceforge.net/byte_of_python.html
  http://pythonstudy.xyz/
  https://wikidocs.net/book/1
  https://opentutorials.org/course/1750
Example Programs
  https://www.programiz.com/python-programming/examples

## Slide 3: Working with Raspberry Pi RPi 설치하기

## Slide 4: Setting Up Raspbery Pi 3
https://www.raspberrypi.org
NOOBS (New Out Of Box Software)
  Download NOOBS image
  Format SD Memory Card using “SD Memory Card Formatter”
  Copy files (NOOBS) to SD Memory Card
  Boot and go!
Raspbian
  https://www.raspberrypi.org/documentation/installation/installing-images/README.md
  Download raspbian image
  Write image to SD card using “etcher”
  For headless setup
    https://core-electronics.com.au/tutorials/raspberry-pi-zerow-headless-wifi-setup.html
    Steps
      Using windows, change device/directory SD card device
      Create “wpa_supplicant.conf” then add the lines 
      Create “ssh”
      Boot
      Figure out IP address of your Pi
      Ssh with login pi and the password raspberry
network={
ssid="SSID"
psk="password"
key_mgmt=WPA-PSK
}

## Slide 5: Keep your pi up-to-date
https://www.raspberrypi.org/learning/software-guide/
  sudo apt-get update
  sudo apt-get upgrade
  sudo apt-get install package

## Slide 6: Python Versions
Python 2 vs Python 3
  https://www.raspberrypi.org/documentation/usage/python/more.md
print “abc” vs print(“abc”)
Reserved words
  https://docs.python.org/3.3/reference/lexical_analysis.html#keywords
  https://docs.python.org/2/reference/lexical_analysis.html#keywords
PEP 8
  http://legacy.python.org/dev/peps/pep-0008/
Running Python
  REPL (Read-Eval-Print-Loop), Interactive top level, Language Shell -- Wikipedia
    $ python3
  Ipython
    $ sudo apt-get install ipython3
    $ ipython3

## Slide 7: Installing Python Libraries
https://www.raspberrypi.org/documentation/linux/software/python.md
APT (Advanced Package Tool)
  To install package from the Python Package Index (PyPI)
    $ sudo apt-get update
    $ sudo apt-get upgrade
PIP
    $ sudo apt-get install python3-pip

## Slide 8: GPIO
https://www.raspberrypi.org/documentation/usage/python/more.md
  $ sudo apt-get install python3-rpi.gpio
import RPi.GPIO as GPIO
import time
GPIO.setmode(GPIO.BOARD) # set board mode to Broadcom
GPIO.setup(3, GPIO.OUT)
GPIO.setup(5, GPIO.OUT)
GPIO.setup(7, GPIO.OUT)
for i in range(0,30):
print(i)
GPIO.output(3, i&0x4)
GPIO.output(5, i&0x2)
GPIO.output(7, i&0x1)
i += 1
time.sleep(0.5)
GPIO.cleanup()

## Slide 9: RPi Configuration
sudo raspi-config
  Do some settings
Remote desktop
  VNC
  http://www.realvnc.com
Setup SSH Keys
  https://dvpizone.wordpress.com/2014/03/02/how-to-connect-to-your-raspberry-pi-using-ssh-key-pairs/
  SSH-2 RSA 2048
  Public Key  ~/.ssh/authorized_keys
  Public Key  Putty configuration

## Slide 10: Python Language

## Slide 11: Python and C
https://blog.udemy.com/python-vs-c/
  The syntax emphasizes code readability by allowing programmers to use 10% of the code required by other languages, such as C.
  Python is often used as a scripting language, but is also extremely effective as a standalone program.

## Slide 12: print function
print(“hello world”)
Print(“hello”, “world”)

## Slide 13: Variables
Basic unit of storing data in a computer program
  counter = 5
  length = height = breadth = 2
  x, y = 2, 3
Type function
  print(type(counter))

## Slide 14: Dynamically Typed
  key = 6
  print(key)
  key = “kim”
  print(key)

## Slide 15: Strongly Typed
  key = 6
  print(key)
  name = “kim” + key
  print(name)

## Slide 16: Data Types
Standard Data Types
  Number
  String
  List
  Tuple
  Dictionary

## Slide 17: Python의 사칙연산
Among
  Int, float, string,

## Slide 18: Integer (정수)
정수의 정의
  http://terms.naver.com/entry.nhn?docId=333...
정수의 연산
  덧셈, 뺄셈, 곱셈
Python에서 일정 범위
집합의 정의
Python에서 정수인지 확인
  print( type(a))

## Slide 19: floating point (소수)
소수
  http://terms.naver.com/entry.nhn?docId=95...
  https://en.wikipedia.org/wiki/Floating_point
    The term floating point refers to the fact
    that a number's radix point can "float“.
Python에서 소수의 표현
  a = 1.2
  b = 3/4

## Slide 20: Break Time
Non sense quiz
  1 + 1 = ?
맥락에 대한 이해가 필요

## Slide 21: Break Time
Non sense quiz
  1 + 1 = ?
Input( )은 항상 string을 준다!

## Slide 22
always try internet search !!!

## Slide 23: String (문자)
print 문에 “,”를 사용해서 여러 개를 프린트하면 한칸씩 자동으로 떼어짐

## Slide 24: String (계속)
“ “도 string!

## Slide 25: 서로 다른 데이터 타입 간의 혼합
Int, Float, Str간의 사칙연산
Data type | 연산자 | Data type | 
Int | + - * | Int | Int
Int | / | Int | Float
Float | + - * / | Int | Float
Str | + | Str |  Str
Str | + - * / | Int, Float |  Error

## Slide 26: 서로 다른 타입 간의 혼합 (계속)
Str 타입을 강제로 변환 시켜 주어야 함
  int(str)
  float(str)
Why?

## Slide 27: Control Structure
Conditionals
  if a<b:
  print(“ok”)
  else:
  print(“not ok”)
Loops
  a, b = 0, 5
  while a<b:
  print(a)
  a += 1
  for i in range(10):
  print(i)

## Slide 28: Indentation
lastname = input('Lastname? ')
point = input('Point? ')
if lastname in { 'kim', 'lee' }:
point = int(point) + 20
print(point)
else:
point = int(point) + 10
print(point)
input('anything else? ')

## Slide 29: Github on RPi

## Slide 30: Install git
$ git init
$ git status
$ git add *.py
edit any file
$ git status
$ git commit -m "my file“
$ git config --global user.email “ekyuho@gmail.com“
$ git config --global user.name “Kyuho Kim“
$ git add t3.py
$ git checkout –b test1
$ git status
edit something
$ git add *
$ git commit –m “hot fix”
$ git checkout master
$ git status
$ git merge test1
$ git status
On RPi
  sudo apt-get install git
Follow beginner’s guide
  https://guides.github.com/activities/hello-world/
  Branch and merging
    https://git-scm.com/book/en/v2/Git-Branching-Basic-Branching-and-Merging

## Slide 31: Work as a team
http://github.com
  create account
  create a project
  link my local repository and remote
    git remote add origin https://github.com/ekyuho/pythonworkshop0821.git
    git push -u origin master

## Slide 32: Fork Python Examples
https://github.com/adaptives/python-examples

## Slide 33: Remote Branching
$ git clone https://github.com/ekyuho/python-examples.git
do some editing
$ git push origin master
check your modification on
https://github.com/ekyuho/python-examples/tree/master/basic_examples

## Slide 34: Programming Projects
파일에서 숫자를 읽어들인다
  숫자의 개수, 합을 계산한다.
  Sequence가 빠진 것들을 찾아내어 출력한다.(1,2,3,5,6) 이라면 4가 빠진것이다.
파일에서 한 라인씩 읽어들인다.
  각 라인에서 숫자와 숫자가 아닌 글자를 구분하여 2 칼람으로 출력한다.
숫자 맞추기 게임을 한다.
  답이 현재 숫자보나 높으면 하얀색LED를, 아래쪽이면 LED를 끄고, 컴퓨터가 이기면 파란색 LED를, 사람플레이어가 이기면 빨간색 LED를 킨다.
Your Idea?